## Slide 1
PCB Defect Detection System
An end-to-end automated quality control solution combining computer vision and deep learning for high-speed, high-accuracy PCB inspection.
AI CircuitGuard

## Slide 2
Solution Overview
Two-Phase Architecture
Architecture: Reference-based Subtraction (Template vs. Test) followed by EfficientNet-B4 CNN.
Architecture Flow
Walk through the simple, linear pipeline: Image Input → Alignment → Masking → Contour → Classification → Annotated Output.
Deliverable: Demonstrate that the system is end-to-end.

## Slide 3
Defect Localization (Modules 1 & 2)
Image Alignment
This is the crucial first step. I used ORB (Oriented FAST and Rotated BRIEF) feature matching combined with RANSAC to calculate the Homography matrix. This ensures the template and test images are perfectly pixel-aligned before subtraction, compensating for camera shift.
preprocessing.py: Uses cv2.ORB_create(500) and cv2.findHomography with cv2.RANSAC.
Masking & Filtering
Defect masks are created using Absolute Difference (cv2.absdiff) followed by Otsu's Thresholding (cv2.THRESH_OTSU). This adaptive thresholding is crucial for robustness against varying lighting.
preprocessing.py: defect_mask = cv2.threshold(difference_map, 0, 255, cv2.THRESH_BINARY + cv2.THRESH_OTSU)
ROI Extraction
Applied simple morphological operations (Opening/Dilation) to clean the mask, then used Contour Detection (cv2.RETR_EXTERNAL) to find defect boundaries. Area filtering (MIN_DEFECT_AREA = 100) was used to remove noise, meeting the "Mask quality, bounding box accuracy" goal.
roi.py: Uses cv2.findContours and filters contours where cv2.contourArea(cnt) < min_area. The resulting ROIs are the labeled input for the CNN.

## Slide 4
Deep Learning Model Training (Module 3)
Model Selection
We selected EfficientNet-B4 via the timm library. This model offers an optimal balance between high classification accuracy and fast inference speed, ideal for manufacturing environments.
training.py: timm.create_model('efficientnet_b4', pretrained=True).
Training Strategy
We used Transfer Learning by leveraging pre-trained ImageNet weights and only retraining the final classification layer (model.classifier). This allowed us to achieve high accuracy quickly with limited defect images.
training.py: Replaced the classifier with nn.Linear(num_ftrs, num_classes). Trained for 30 epochs with 5e-5 learning rate.
Data Flow
The model was trained on 128 × 128 RGB images that were normalized using ImageNet means/stds.
training.py: transforms.Normalize(NORM_MEAN, NORM_STD).

## Slide 5
Results & Evaluation (Module 4)
Accuracy Metric
We successfully met the target, achieving 97.5% classification accuracy.
Target: ≥ 97\% test accuracy.
Performance Metrics
Spur and Spurious Copper were harder to distinguish.
Deliverable: Accuracy, Loss, Confusion Matrix.
Inference Logic
Prediction uses torch.softmax to get probabilities, ensuring the confidence score is reliable.
module4.py: Uses torch.softmax(output, dim=1) and extracts the confidence with torch.max.

## Slide 6
Backend Pipeline (Module 6)
Master Function
The full_inference_pipeline in mod6.py is the single function responsible for coordinating all modules. It takes the raw test image and outputs the annotated result and the log data.
mod6.py: Contains the entire flow: align_and_subtract → extract_rois → predict_single_roi → draw_annotations.
Annotation
Final results (prediction + bounding box coordinates) are used by draw_annotations to visually label the defects on the image. We used cv2.rectangle and cv2.putText for this final visualization step.
mod6.py: The draw_annotations function uses cv2.FONT_HERSHEY_SIMPLEX for text labeling.
Speed Metric
The integrated system meets the core speed requirement.
Target Metric: ≤ 5 seconds per image.

## Slide 7
Frontend UI & Export (Modules 5 & 7)
User Interface
The frontend uses Streamlit for rapid deployment and ease of use. It takes a single image upload and displays the annotated image and the detailed defect log.
app.py: Uses st.file_uploader, st.image, and st.dataframe.
Export Feature
This is a key deliverable. The system allows users to download two critical files for quality assurance documentation: 1) The Annotated Output Image (JPEG), and 2) The Detailed Defect Log (CSV).
app.py: Uses st.download_button to export the image bytes and the Pandas DataFrame (df_log) converted to CSV string.
Final Evaluation
Conclude by confirming the successful delivery of a Professional-quality outcome with a fully functional UI and robust export features.
Evaluation: Fully functional UI with successful export feature.

## Slide 8
Thank You Everyone!
- Yashika Agarwal